## Slide 1
Device as a Service
Lenovo vs Apple: side by side
flynas options for the new HQ endpoint service
ITEUS · October 2026
vs

## Slide 2
Lenovo vs Apple at a glance
Both offer the same service model; the difference is the platform
Area | Lenovo (ThinkPad, Windows) | Apple (Mac, via KSA partner)
Platform | Windows 11 Pro on Intel or AMD | macOS on Apple M5 or M5 Pro
Contract holder | Lenovo KSA under TruScale DaaS | Apple Authorised Enterprise Reseller (TBC)
Change for users | None: same OS, apps and device families | New OS; Windows-only apps need B.1 or Windows 365
Memory as quoted | 32GB on every laptop | 24GB on every Mac
Desk kit | Thunderbolt dock and two monitors | Belkin adapter, one 27" monitor; dock Director up
Touch / 2-in-1 | ThinkPad X1 2-in-1 Gen 11 | No touch Mac: B.1 tier or an iPad
Failed drive | Keep Your Drive: drive stays with flynas | Built-in SSD: FileVault and remote wipe
Fleet buyback | Lenovo Asset Recovery Services, direct | Partner trade-in and ITAD
Operations tablets | Not offered | iPads for flight deck, cabin, engineering, stations
Lenovo is the low-change option; Apple adds iPads and 24GB on every Mac, but needs app testing.
As written in each discussion deck. Lenovo is quoted at 32GB and two monitors, Apple at 24GB and one, so align specs before comparing price.

## Slide 3
Device lineup by policy tier
Today’s fleet against each vendor’s 2026 proposal
Policy tier | Today | Lenovo 2026 | Apple 2026 | Memory: Lenovo / Apple
Officer to Sr Mgr, 13-14" | ThinkPad E14 / L14 | ThinkPad L14 (2026) | MacBook Air 13", M5 | 32GB / 24GB
Officer to Sr Mgr, 15-16" | ThinkPad E16 / L16 | ThinkPad L16 (2026) | MacBook Air 15", M5 | 32GB / 24GB
Director to VP | ThinkPad X1 Carbon | X1 Carbon Gen 14 | MacBook Pro 14", M5 | 32GB / 24GB
Touch / 2-in-1 | ThinkPad X1 Yoga | X1 2-in-1 Gen 11 | No Mac: B.1 tier or iPad | 32GB / n/a
C-Level | Per IT assessment | Not a separate tier | MacBook Pro 14"/16", M5 Pro or Max | Per IT assessment
Desktop / shared desk | ThinkCentre Neo 50 AIO | ThinkCentre Neo AIO | iMac 24", M4 | TBC / 24GB
Specialists | Custom / workstation | ThinkStation P-series | Mac Studio / MacBook Pro 16" | Per requirement
All laptops 1TB SSD. Lenovo is quoted at 32GB for everyone; Apple at 24GB for everyone.
Lenovo deck uses Officers / Managers and above; mapped here to Appendix B tiers. Models and prices to be confirmed by each vendor.

## Slide 4
Processors: Intel or AMD vs Apple silicon
Both are current-generation AI PC chips; the platform is the real choice
Lenovo ThinkPad
Intel or AMD, same chip every tier
Intel Core Ultra 7 356H, 16 cores, up to 4.7 GHz
AMD Ryzen AI 7 PRO 350, 8 cores, up to 5.0 GHz
AI NPU up to 50 TOPS, Copilot+ PC class
Manage Intel vPro or AMD PRO, Windows 11 Pro
Fit Runs every current flynas app as today
Apple Mac
M5 for all tiers, M5 Pro for C-Level
M5 10-core CPU, MacBook Air and Pro, Officer to VP
M5 Pro 15 or 18-core CPU, MacBook Pro for C-Level
AI 16-core Neural Engine, GPU Neural Accelerators
Manage Apple Business Manager with Intune or Jamf
Fit Windows-only apps need B.1 or Windows 365
Ask both vendors for pilot units so ITEUS can test our core apps on each platform before deciding.

## Slide 5
Desk kit, support and lifecycle
Service terms side by side
Area | Lenovo | Apple
Monitors | Two 24" or 27" per desk | One 27" Lenovo ThinkVision USB-C
Dock / adapter | Thunderbolt dock at every desk | Belkin 11-in-1; Lenovo dock for Director up
Peripherals | Headset, keyboard and mouse | Magic Keyboard, Mouse or Trackpad, headset
Deployment | Factory image and Autopilot | Zero-touch via Apple Business Manager, Intune
Asset tracking | Device Intelligence, Service Connect, Ivanti | ABM with Intune or Jamf, feeding Ivanti
Support abroad | International Warranty; onsite or depot | AppleCare for Enterprise, Apple service network
IT training | Certification for in-house part swaps | Apple certifications, Independent Repair Provider
Lifecycle | 36 months, optional 4th year, buyout | Same, with Mac resale value lowering the rate
Same model from both: one per-seat fee, 36-month refresh, NIST 800-88 wipe certificates as NCA evidence.
Desk kit as written in each deck; the Lenovo two-monitor desk is above the Appendix B standard.

## Slide 6
Strengths and watch-outs
Where each option is stronger, and what to plan for
Lenovo: strengths
No change for users or ITEUS. Touchscreen 2-in-1s, Keep Your Drive, and Lenovo buys back its own fleet directly.
Apple: strengths
24GB on every Mac. iPads for operations on the same contract. Mac resale value can lower the rate.
Lenovo: watch-outs
Quoted above policy (32GB for all, two monitors), which raises the price. No tablet offer. Some chassis Intel only.
Apple: watch-outs
Windows-only apps need B.1 or Windows 365. No touch Mac, no drive retention. Contract via a reseller.

## Slide 7
Decision points and next steps
What flynas needs to settle before choosing
To decide
Platform: Windows, Mac, or mixed by role
Which Windows-only apps block a Mac move
Touch users: 2-in-1 laptop or iPad
Is an operations iPad program in scope?
Is drive retention required by policy?
Keep or drop Mac Studio for specialists
Next steps
Both vendors quote the same spec per seat
Pilot units of each for ITEUS app testing
Compare cost per seat at 36 and 48 months
Confirm onsite cover in KSA and stations
Recommendation to Finance and Procurement
Price locked for the full term, added seats too
Goal: like-for-like, per-seat prices from both vendors, so the choice is about platform and service.

## Slide 8
Thank You